## Slide 1: A Survey on SGX Enclave Privileged Side-Channel Attacks
Amin Fallahi
Ph.D. Student
Department of Electrical Engineering and Computer Science
MAY 14, 2018

## Slide 2: Contents
Introduction
Attacks
Defenses
Analysis
Conclusion
Department of Electrical Engineering and Computer Science

## Slide 3: Introduction
Computing environment
  Shared resources executing user programs
Security inside the cloud
  A hardware solution needed
Intel SGX
  Secure user code and data in the public cloud
  Protecting data inside the enclave
Privileged Operating System
  Kernel space, hardware control
Department of Electrical Engineering and Computer Science

## Slide 4: Introduction
17 new instructions
Enclave created by OS
  Contiguous physical memory
  Base address randomly assigned from EPC
Hardware level memory encryption engine
Virtual to physical address translation done by OS
Interrupt ⇨ context switch – AEX
ECALLs & OCALLs
Intel SGX
Department of Electrical Engineering and Computer Science

## Slide 5: Introduction
Side-Channels
  Attacks by analyzing system behavior
  Cache attacks: Monitoring cache accesses
  Timing attacks: Measuring time between computations
  Page-fault attack: Monitoring page-faults and analyzing the pattern
Attack Model
  Enclave protected by SGX
    No stranger has the key
  Operating System can manage task queues, interrupts, and exceptions
  Viewing data transfer between memories
  Program pinned to one core, no excessive interrupts, isolated
Department of Electrical Engineering and Computer Science

## Slide 6: Attacks
Intentional Cache-Misses ⇨ Make program access memory
Time, trace, access patterns
Prime+Probe
  Prime: attacker executes conflicting cache lines ⇨ cache miss
  Probe: executing all the cache lines and measuring execution time
Cache-Based Attacks
Department of Electrical Engineering and Computer Science

## Slide 7: Attacks
RSA key extraction
  Modular exponentiation
  Large e, d, and n such that
  Knowing m, e, and n it is extremely difficult to find d
Square and multiply
  Typical algorithm ⇨ find the exponent
  Secret dependent memory accesses
Cache-Based Attacks
Department of Electrical Engineering and Computer Science

## Slide 8: Attacks
Basic page-fault attack
  AEX on fault ⇨ base address of faulting page revealed
  Cause intentional page faults ⇨ obtain page level trace
  Monitor a specific page
Page Table Based Attacks
Department of Electrical Engineering and Computer Science

## Slide 9: Attacks
Problem: page-faults cause a high overhead => attack detection
  Solution: Use page-table access and dirty bits
Problem: TLB caches PTEs and flags are not updated in PT
  Solution: Flush TLB using an IPI
Problem: Lots of IPIs
  Solution: Time difference between two repeatedly accessed pages ⇨ different input dependent paths between pages ⇨ no interrupts between two pages
Problem: Still interrupts!
  Solution: TLB is shared between two hyperthreads on same core ⇨ invalidate TLB entries ⇨ no IPIs
Page Table Based Attacks
Department of Electrical Engineering and Computer Science

## Slide 10: Attacks
Flush+Reload
  Flush a memory line and wait for victim to access it
Flush+Flush
  Flush a cache line using clflush instruction
DRAMA
  Caching disabled
  Allocate two memory lines with different virtual addresses but same physical address
  Regularly access one of the memory lines
Cache-DRAM
  Prime+Probe + DRAMA
Other Attacks
Department of Electrical Engineering and Computer Science

## Slide 11: Defenses
Basic approach: Pin code/data to cache
Using Intel TSX
  Introduced with Haswell
  Critical sections management
  Monitoring serialization
  Restricted Transactional Memory
    New Instruction set interface
Cloak
  Preload code/data
  Execute algorithm inside transaction
Defense against cache-based attacks
Department of Electrical Engineering and Computer Science

## Slide 12: Defenses
T-SGX: run code inside transaction => page fault => attack detection => program termination
Problem: Frequent timer interrupt
  Program take too long => exception => never terminate
Problem: TSX buffers all memory changes inside cache
  single transaction, lots of accesses => cache conflict => transaction abort
Break program into tiny blocks
  Problem: transaction setup has cost => performance
Merge continuous blocks
Problem: boundaries leak
  Solution: springboard
Defense against page table based attacks
Department of Electrical Engineering and Computer Science

## Slide 13: Defenses
Déjà vu
  Reference clock thread inside a transaction
Shinde et al.
  Deterministic page access profile
  Introducing fake acceses
SGX-Shield
  ASLR
ZeroTrace
  Use of ORAM + SGX
Dr. SGX
  Data location randomization
Other defense methods
Department of Electrical Engineering and Computer Science

## Slide 14: Analysis
Cloak
  Makes cache-pinning possible to some extent
  Execution time can leak
  Aborts do not cancel concurrent memory accesses
  Execution behavior and branch prediction uncertainties
T-SGX
  Attacks based on monitoring flags are possible
Bottom line
  Transaction based defenses usually come with high overload and low utilization, and need isolation
Other methods
  Attack detection methods ⇨ Unreliable
  Shuffling memory ⇨ expensive
  ORAM (make addresses input-independent) ⇨ expensive
Department of Electrical Engineering and Computer Science

## Slide 15: Analysis
The perfect solution?
  Remove all branches and conditional code
  Pin data/code to cache and TLB
  CAT+SGX
  Non-shared non-cached secure memory element
Most of defenses either work on page table based attacks or cache-based attacks
ORAM performance optimization
Page table flags monitoring attacks
Department of Electrical Engineering and Computer Science

## Slide 16: Conclusion
We studied multiple attacks and defenses
Still no robust defense
Attack are emerging
Open to research
Department of Electrical Engineering and Computer Science

## Slide 17: References
Michael Schwarz, Samuel Weiser, Daniel Gruss, Clémentine Maurice, and Stefan Mangard. 2017. Malware guard extension:UsingSGXtoconcealcacheattacks.InInternational Conference on Detection of Intrusions and Malware, and Vulnerability Assessment.Springer,3–24.
Ferdinand Brasser, Urs Mu¨ller, Alexandra Dmitrienko, Kari Kostiainen, Srdjan Capkun, and AhmadReza Sadeghi. 2017. Software grand exposure: SGX cache attacks are practical. arXiv preprint arXiv:1702.07521 (2017), 33.
Daniel Gruss, Julian Lettner, Felix Schuster, Olya Ohrimenko, Istvan Haller, and Manuel Costa. 2017. Strong and efficient cache side-channel protection using hardware transactional memory. In USENIX Security Symposium.
Ming-Wei Shih, Sangho Lee, Taesoo Kim, and Marcus Peinado. 2017. T-SGX: Eradicating controlled channel attacks against enclave programs. In Proceedings of the 2017 Annual Network and Distributed System Security Symposium (NDSS), San Diego, CA.
Jo Van Bulck, Nico Weichbrodt, Ru¨diger Kapitza, Frank Piessens, and Raoul Strackx. 2017. Telling your secrets without page faults: Stealthy page table-based attacks on enclaved execution. In Proceedings of the 26th USENIX Security Symposium. USENIX Association.
Wenhao Wang, Guoxing Chen, Xiaorui Pan, Yinqian Zhang, Xiaofeng Wang, Vincent Bindschaedler, Haixu Tang, and Carl A. Gunter. 2017. Leaky Cauldron on the Dark Land: Understanding Memory Side-Channel Hazards in SGX. 2421–2434.
Department of Electrical Engineering and Computer Science

## Slide 18: References
[1] Ferdinand Brasser, Srdjan Capkun, Alexandra Dmitrienko, Tommaso Frassetto, Kari Kostiainen, Urs Mu¨ller, and Ahmad-Reza Sadeghi. 2017. DR. SGX: Hardening SGX Enclaves against Cache Attacks with Data Location Randomization. arXiv preprint arXiv:1709.09917 (2017). [2] Ferdinand Brasser, Urs Mu¨ller, Alexandra Dmitrienko, Kari Kostiainen, Srdjan Capkun, and AhmadReza Sadeghi. 2017. Software grand exposure: SGX cache attacks are practical. arXiv preprint arXiv:1702.07521 (2017), 33. [3] Sanchuan Chen, Xiaokuan Zhang, Michael K Reiter, and Yinqian Zhang. 2017. Detecting privileged side-channel attacks in shielded execution with D´ej´a Vu. In Proceedings of the 2017 ACM on Asia Conference on Computer and Communications Security. ACM, 7–18. [4] Oded Goldreich. 1987. Towards a theory of software protection and simulation by oblivious RAMs. In Proceedings of the nineteenth annual ACM symposium on Theory of computing. ACM, 182–194. [5] Oded Goldreich and Rafail Ostrovsky. 1996. Software protection and simulation on oblivious RAMs. Journal of the ACM (JACM) 43, 3 (1996), 431–473. [6] Daniel Gruss, Julian Lettner, Felix Schuster, Olya Ohrimenko, Istvan Haller, and Manuel Costa. 2017. Strong and efficient cache side-channel protection using hardware transactional memory. In USENIX Security Symposium. [7] Daniel Gruss, Cl´ementine Maurice, Klaus Wagner, and Stefan Mangard. 2016. Flush+ Flush: a fast and stealthy cache attack. In International Conference on Detection of Intrusions and Malware, and Vulnerability Assessment. Springer, 279–299. [8] Mehmet Kayaalp, Nael Abu-Ghazaleh, Dmitry Ponomarev, and Aamer Jaleel. 2016. A high-resolution side-channel attack on last-level cache. In Proceedings of the 53rd Annual Design Automation Conference. ACM, 72. [9] Rafail Ostrovsky. 1990. Efficient computation on oblivious RAMs. In Proceedings of the twenty-second annual ACM symposium on Theory of computing. ACM, 514–523. [10] Dag Arne Osvik, Adi Shamir, and Eran Tromer. 2006. Cache attacks and countermeasures: the case of AES. In Cryptographers’ Track at the RSA Conference. Springer, 1–20. [11] Peter Pessl, Daniel Gruss, Cl´ementine Maurice, Michael Schwarz, and Stefan Mangard. 2016. DRAMA: Exploiting DRAM Addressing for Cross-CPU Attacks.. In USENIX Security Symposium. 565–581. [12] Sajin Sasy, Sergey Gorbunov, and Christopher Fletcher. 2017. ZeroTrace: Oblivious memory primitives from Intel SGX. In Symposium on Network and Distributed System Security (NDSS). [13] Jaebaek Seo, Byounyoung Lee, Seongmin Kim, Ming-Wei Shih, Insik Shin, Dongsu Han, and Taesoo Kim. 2017. SGX-Shield: Enabling address space layout randomization for SGX programs. In Proceedings of the 2017 Annual Network and Distributed System Security Symposium (NDSS), San Diego, CA. [14] Ming-Wei Shih, Sangho Lee, Taesoo Kim, and Marcus Peinado. 2017. T-SGX: Eradicating controlledchannel attacks against enclave programs. In Proceedings of the 2017 Annual Network and Distributed System Security Symposium (NDSS), San Diego, CA. [15] Shweta Shinde, Zheng Leong Chua, Viswesh Narayanan, and Prateek Saxena. 2015. Preventing your faults from telling your secrets: Defenses against pigeonhole attacks. arXiv preprint arXiv:1506.04832 (2015). [16] Eran Tromer, Dag Arne Osvik, and Adi Shamir. 2010. Efficient cache attacks on AES, and countermeasures. Journal of Cryptology 23, 1 (2010), 37–71. [17] Jo Van Bulck, Nico Weichbrodt, Ru¨diger Kapitza, Frank Piessens, and Raoul Strackx. 2017. Telling your secrets without page faults: Stealthy page table-based attacks on enclaved execution. In Proceedings of the 26th USENIX Security Symposium. USENIX Association. [18] Wenhao Wang, Guoxing Chen, Xiaorui Pan, Yinqian Zhang, Xiaofeng Wang, Vincent Bindschaedler, Haixu Tang, and Carl A. Gunter. 2017. Leaky Cauldron on the Dark Land: Understanding Memory Side-Channel Hazards in SGX. 2421–2434. [19] Yuval Yarom and Katrina Falkner. 2014. FLUSH+ RELOAD: A High Resolution, Low Noise, L3 Cache Side-Channel Attack.. In USENIX Security Symposium
Department of Electrical Engineering and Computer Science